## Slide 1: Web-based Class Project on Geoenvironmental Remediation
Report prepared as part of course
CEE 549: Geoenvironmental Engineering
Winter 2013 Semester
Instructor: Professor Dimitrios Zekkos
Department of Civil and Environmental Engineering
University of Michigan
PHYTOREMEDIATION
Prepared by:
Darin McLeskey
Stefano Bruni
With the Support of:

## Slide 2: Concept/ Description
Within Bioremediation
Vegetation aides in contaminant breakdown/removal
Driven by nature, utilizes less inputs
Generally lower costs, but longer time
Positive public perception
Rapid growth rate

## Slide 3: Theoretical Background
Many different biological processes
Plant root/ soil contact important
Rhizofiltration – Room membrane filtration
Phytodegragation – organic metabolization
Phytoaccumulation – inorganic accumulation
Rhizodegradation – breakdown and accumulation in root membranes, generally aided by microbes
Phytovolatilization – conversion to volatile forms
Phytoextraction – similar to pump and treat

## Slide 4: Theoretical Background

## Slide 5: Applicability
Polishing treatment
Hydrocarbon residuals
Heavy metals
Chlorinated solvents
Pesticides/Herbicides/Radionuclides
Phenols/Munitions
Kow ratios of 1-3.5 have greatest potential
Low organic content in soil
Less than 10’ of contamination

## Slide 6: Advantages
Soil stabilization and pollutant fixation
Lower cost and less invasive
Performed in-situ
Aesthetically pleasing with public appeal
Excellent for agricultural soil damaged by dispersed industrial pollution

## Slide 7: Disadvantages
Not fully embraced by government and industry
Depth limitation
Slow (3-5 year) timeline
Designs are very site-specific
Plant combinations can use more research
Equipment is often far from urban areas
Precaution for food-chain access

## Slide 8: Field Setup
Define species
Irrigation/ nutrients
Treatment
Monitoring
Harvesting
Monitoring
Closure
Some process loops

## Slide 9: Plant Selection
Define type and quantity
Varying soil types
Select high biomass yield
Hyperaccumulator species
Background nutrient levels

## Slide 10: Application

## Slide 11: Irrigation/ Soil Amendment
Irrigation may be necessary
Water encourages pollutant dissolution
Repeated species reuse exhausts pollutants
pH adjustment, chelating for metal solubility

## Slide 12: Monitoring
Continual sampling plan
  Soil
  Water
  Crops
Dynamic treatment strategy

## Slide 13: Harvesting
Mass balance for treatment efficiency
Accumulation in various plant parts
Composting or processing
Incineration
Used as “bio-enhanced” feedstock
Mineral ore potential

## Slide 14: Cost
Low level: $10-15/ ton
Off site: $200-600/ ton
500 ppm lead example:
  $300,000 acre for disposal
  $110,000 for phytoremedation
Opportunity costs!

## Slide 15: Due Care Considerations
Erosion prevention
Dust migration
Biomass in food chain
Pest/ rodent deterrents
Limit access to area

## Slide 16: Modeling and Combinations
Four main models:
  Numerical and Analytical
  Developed in mid-90s
  All have severe limitations
Combined with other methods:
  Bioremediation & inoculation
  Polishing treatment

## Slide 17: OneSITE WWTP – Woodburn, OR
10,000 Poplar trees over 400 acres
Abandoned sludge lagoon
Stabilize waste/ buffer
Alternative to 5 million gallon untreated release
$2.5 million cost
$800,000 harvest every 10 years

## Slide 18: Radionuclide Extraction - Chernobyl
Fallout in sandy soil
Indian mustard, corn, peas, artichoke, sunflowers
Only artichoke and sunflowers were effective
Decrease only over 3 weeks
Chelating increased uptake 20x
Incineration used for 90% waste reduction

## Slide 19: Lead Phytoremediation – NJ
Lead-acid battery factory
4500 sq. ft.
Close to church, school, homes
XRF for continual monitoring
Indian Mustard – 3.5” pots
EDTA for lead solubility
6 week growing cycle

## Slide 20: Lead Phytoremediation - Results

## Slide 21: Local Example – Milwaukee Junction
Historic industrial area
High vacancy
Near transit and new developments
5-10 year development timeline
Dispersed pollutants

## Slide 22: Local Example – Milwaukee Junction
Summer pilot project
  Van Antwerp Coal Yard
  Later automotive service center
  Lead, arsenic, hydrocarbons
  Mapping entire district

## Slide 23: Local Example – Milwaukee Junction
Soil testing and delineation
Sunflower & Indian Mustard interplanting
Near incinerator facility
Indoor hydroponics and retail nursery
End use – BHARN
  Brush Hydroponics/ Aquaculture Retail Nursery

## Slide 24: Local Example – Milwaukee Junction
Collaboration:

## Slide 25: References
Sharma, H.D., Reddy K.R. (2004). “Geoenvironmental Engineering.” Jon Wiley & Sons, Hoboken, New Jersey, 478-485
Doty, S.L. (2008). “Enhancing phytoremediation through the use of transgenics and endophytes.” New Phytologist (2008) 179: 318–333
Blaylock, M.J., Elless, M.P., Huang, J.W., Dushenkov, S.M. (1999). “Phytoremediation of Lead-Contaminated Soil at a New Jersey Brownfield Site.” Remediation, summer 1999; 93-101
Chaney, R.L., Broadhurst, L., Centofanti, T. “Phytoremediation of Soil Trace
Elements.” Bioavailability, Risk Assessment and Remediation; 311-352
Rock, S.A., Sayre, P.G. (1998) “Phoremediation of Hazardous Wastes: Potential Regulatory Acceptability.” Remediation, autumn 1998; 5-17
Zadrow, J.J. (1999). “Recent Applications of Phytoremediation Technologies.” Remediation, spring 1999; 29-36
Mudhoo, A. (2011). “Phytoremediation of Cadmium: A Green Approach.”
Gupta et al. “Phytoremediation: An Efficient Approach for Bioremediation of Organic and Metallic Ions Pollutants.” Bioremediation and Sustainability; 213-240
Dushenkov, S., Mikheev, A., Prokhnevsky A., Ruchko, M., and Sorochinsky, B., Phytoremediation of radiocesium-contaminated soil in the vicinity of Chernobyl, Ukraine, Environ. Sci. Technol., Vol. 33, pp. 469-475, 1999.

## Slide 26: More Information
More detailed technical information on this project can be found at:
http://www.geoengineer.org/education/web-based-class-projects/geoenvironmental-remediation-technologies