## Slide 1: Web-based Class Project on Ground Improvement
Report prepared as part of course
CEE 542: Soil and Site Improvement
Winter 2014 Semester
Instructor: Professor Dimitrios Zekkos
Department of Civil and Environmental Engineering
University of Michigan
Prefabricated Vertical Drains
Prepared by:
Jenna Scorza
Greg Fox
With the Support of:

## Slide 2: Prefabricated Vertical Drains Greg Fox & Jenna Scorza

## Slide 3: Introduction
Expediting consolidation of slow draining soils
Shorten pore water travel distance
Coupled with surcharge
Horizontal flow

## Slide 4: History
1920s: sand drain patented
1930s: band-shaped vertical drain made of cardboard core and paper filter jacket
1980s: plastic PVD introduced and replaced predecessors

## Slide 5: Features
Channeled plastic core wrapped with geotextile
Core:
Support for filter fabric
Provide longitudinal flow paths
Resistance to stretching and buckling
Jacket:
Acts as filter

## Slide 6: Features Equivalent Diameter
Hanso 1979
Rixner 1986
Oblong shape, theories available derived for circular shape
Many equations have been suggested
Different assumptions = different results

## Slide 7: Features Independent Evaluation By Richard P. Lomg & Alvaro Covo
Analog Field Plotter
  Electrical potential to hydraulic head
  Electrical current to flow of water
Results agree with Suits et al. 1986
  Flow Net for Flow to Oblong Drain from Circular Surface

## Slide 8: Benefits
Decrease primary consolidation time period
Decrease surcharge required for precompression
Increase rate of strength gain and stability
Compared to Sand Drains
  Economic competitiveness
  Less soil disturbance
  Improved speed and simplicity of installation
  Feasible nonvertical orientation and underwater installation

## Slide 9: Disadvantages
Pre-excavation may be needed for very dense or stiff fills
Ground distrubance may not be tolerable in sensitive soils
Winter Considerations
  Frost line 3ft depth in MidWest
  Frost can reduce drain discharge
    Build up pack pressure
    Retard settlement development
    Lead to false premise that primary consolidation has reached an end

## Slide 10: Suitable Soils
Implemented in soils that are moderately to highly compressible under static loading
Inorganic silts and clays of low to moderate sensitivity
Organic layers
Decomposed peat
Clayey and silty sands
Dredge spoils
Varved cohesive deposits

## Slide 11: Installation
Steel mandrel encasing wick drain
Driven with vibrating (or static) force by stitcher
Drain anchored at desired depth, mandrel removed
Wick drain cut at surface
Depth and Width of drains selected based on soil stratigraphy and project specifications

## Slide 12: Depth and Width of Installation
Drain should be extended into any available pervious soil layer below preconsolidation stress margin to assure discharge of water
Drains should be distributed across the entire footprint of an embankment and a small distance beyond

## Slide 13: Design of Drains
Coefficient of Consolidation for Horizontal Drainage, ch
ch = (kh / kv)*cv
cv from 1-D consolidation test
Coefficient of Permeability for Horizontal Seepage, kh
kh / kv ~ 1 (conservative estimate)
lab/field testing
Coefficient of Permeability in Horizontal Direction of Disturbed Soil, ks
kh/ks ~ 1~5
varies with soil sensitivity
Drain Influence Zone
D = 1.13s (Square)
D = 1.05s (Triangular)

## Slide 14: Effectiveness of PVDs
Water Flow into Drain
  Hydraulic Conductivity
  Smear Zone
Discharge Capacity
  Design
  Installation
  Clogging
  Bending/Kinking
  Biological Degradation

## Slide 15: Water Flow into Drain Hydraulic Conductivity
k of surrounding soil will control water flow into drain

## Slide 16: Water Flow into Drain Smear Zone Development
Results from Installation of drains
  Mandrel to clamp drain
  Anchor Plate
    Keep drain in place
    Prevent soil entering through bottom of drain

## Slide 17: Water Flow into Drain Smear Zone Idealization

## Slide 18: Water Flow into Drain Smear Zone Generalities
Larger Mandrel = Larger Smear Zone
Shape of Mandrel affects shape of smear zone
Square/Circular Mandrel = square/circular zone
Rectangular mandrel = ellipsoidal zone
Outer boundary of zone range 4~18 times mandrel radius
Ratio of hydraulic conductivity of undisturbed soil to smear zone ranges from 1~5

## Slide 19: Discharge Capacity Design & Installation
Design
  Cross Sectional Area - core available for flow
  Geosynthetic materials used
Installation
  Presents critical case for the mechanical properties of drain
    ASTM Grab, Puncture Tests

## Slide 20: Discharge Capacity Clogging & Biological Activity
Clogging
  Filter - Apparent Opening Size (AOS)
  Larger drain channel = less clogging
Biological Activity
  Depending on duration of project

## Slide 21: Discharge Capacity Bending/Kinking of Drain
Consolidation of soil results in bending and/or kinking of drain
Whether drain bends or kinks depends on
  Flexibility of drain (more flexibility leads to greater reduction in discharge capacity)
  Modulus of surrounding soil

## Slide 22: Discharge Capacity Bending/Kinking of Drain

## Slide 23: Discharge Capacity Bending/Kinking of Drain

## Slide 24: Recent Development & Future of PVDs
Recent Development
  Use of electronics for quality control
    Depth, Installation Force, GPS coordinates, date/time info.
    Necessity of such equipment depends on project
Future
  Precision of targeted geosynthetic function
  Understanding of smear zone and drain deformation are largest areas for improvement

## Slide 25: Questions?

## Slide 26: More Information
More detailed technical information on this project can be found at:
http://www.geoengineer.org/education/web-based-class-projects/select-topics-in-ground-improvement